## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 3 Transport Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (April 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on QUIC, CUBIC, delay-based congestion control
lighter header font

## Slide 2: Transport services and protocols
provide logical communication between application processes running on different hosts
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
transport protocols actions in end systems:
  sender: breaks application messages into segments, passes to network layer
  receiver: reassembles segments into messages, passes to application layer
two transport protocols available to Internet applications
  TCP, UDP
Notes: By logical communication , we
mean that from an application’s perspective, it is as if the hosts running the processes
were directly connected; in reality, the hosts may be on opposite sides of the
planet, connected via numerous routers and a wide range of link types. Application
processes use the logical communication provided by the transport layer to send
messages to each other, free from the worry of the details of the physical infrastructure
used to carry these messages.
Let’s look at each of these three (logical communications, actions,

## Slide 3: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
Sender:
app. msg
is passed an application-layer message
determines segment header fields values
creates segment
passes segment to IP
transport
Th
Th
app. msg

## Slide 4: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
transport
Receiver:
app. msg
extracts application-layer message
checks header values
receives segment from IP
Th
app. msg
demultiplexes message up to application via socket

## Slide 5: Two principal Internet transport protocols
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
TCP: Transmission Control Protocol
  reliable, in-order delivery
  congestion control
  flow control
  connection setup
UDP: User Datagram Protocol
  unreliable, unordered delivery
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees

## Slide 6: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 7
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg

## Slide 8
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
HTTP msg

## Slide 9
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
HTTP msg
Ht
Hn
HTTP msg

## Slide 10
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
Hn

## Slide 11
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client1
client2
P-client1
P-client2

## Slide 12: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:

## Slide 13: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 14: Connectionless demultiplexing
Recall:
when creating socket, must specify host-local port #:
DatagramSocket mySocket1 = new DatagramSocket(12534);
when receiving host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP/UDP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at receiving host

## Slide 15: Connectionless demultiplexing: an example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?

## Slide 16: Connection-oriented demultiplexing
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
server may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
  each socket associated with a different connecting client
demux: receiver uses all four values (4-tuple) to direct segment to appropriate socket

## Slide 17: Connection-oriented demultiplexing: example
transport
application
physical
link
network
P1
transport
application
physical
link
P4
transport
application
physical
link
network
P2
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
server: IP address B
Three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets

## Slide 18: Summary
Multiplexing, demultiplexing: based on segment, datagram header field values
UDP: demultiplexing using destination port number (only)
TCP: demultiplexing using 4-tuple: source and destination IP addresses, and port numbers
Multiplexing/demultiplexing happen at all layers

## Slide 19: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 20: UDP: User Datagram Protocol
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
no connection establishment (which can add RTT delay)
simple: no connection state at sender, receiver
small header size
no congestion control
  UDP can blast away as fast as desired!
  can function in the face of congestion
Why is there a UDP?
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others

## Slide 21: UDP: User Datagram Protocol
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
  HTTP/3
if reliable transfer needed over UDP (e.g., HTTP/3):
  add needed reliability at application layer
  add congestion control at application layer

## Slide 22: UDP checksum
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  Not equal - error detected
  Equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 23: Internet checksum: an example
example: add two 16-bit integers
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1

## Slide 24: Internet checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!

## Slide 25: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 26: Principles of reliable data transfer
sending process
data
receiving process
data
reliable channel
application
transport
reliable service abstraction
Notes: note arrows through reliable data transfer channel is just one way – reliably send from sender to receiver

## Slide 27: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
sending process
data
receiving process
data
reliable channel
application
transport
reliable service abstraction
Notes: Spend some time talking about how its to the sender and receiver side protocol that IMPLEMENTS reliable data transfer
Communication over unreliable channel is TWO-way: sender and receiver will exchange messages back and forth to IMPLEMENT one-way reliable data transfer

## Slide 28: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
Complexity of reliable data transfer protocol will depend (strongly) on characteristics of unreliable channel (lose, corrupt, reorder data?)
Notes: So we have a sender side and a receiver side. How much work they’ll have to do depends on the IMPAIRMENTS introduced by channel – if the channel is perfect – no problem!

## Slide 29: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
Sender, receiver do not know the “state” of each other, e.g., was a message received?
unless communicated via a message
Notes: Here’s a point of view to keep in mind – it’s easy for US to look at sender and receiver together and see what is happening. OH – that message sent was lost.
But think about it say from senders POV How does the sender know if its transmitted message over the unreliable channel got though?? ONLY if receiver somehow signals to the sender that it was received.
The key point here is that one side does NOT know what is going on at the other side – it’s as if there’s a curtain between them. Everything they know about the other can ONLY be learned by sending/receiving messages.
Sender process wants to make sure a segment got through. But it can just somehow magically look through curtain to see if receiver got it. It will be up to the receiver to let the sender KNOW that it (the receiver) has correctly received the segment.
How will the sender and receiver do that – that’s the PROTOCOL.
Before starting to develop a protocol, let’s look more closely at the interface (the API if you will)

## Slide 30: Reliable data transfer protocol (rdt): interfaces
sending process
data
receiving process
data
unreliable channel
sender-side
implementation of rdt reliable data transfer protocol
receiver-side
implementation of rdt reliable data transfer protocol
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
data
Header
data
Header
rdt_send(): called from above, (e.g., by app.). Passed data to deliver to receiver upper layer
udt_send(): called by rdt
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on receiver side of channel
deliver_data(): called by rdt to deliver data to upper layer
Bi-directional communication over unreliable channel
data
packet

## Slide 31: Reliable data transfer: getting started
We will:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow in both directions!
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions
use finite state machines (FSM) to specify sender, receiver
Notes: SO let’s get started in developing our reliable data transfer protocol, which we’ll call rdt (need a good acronym for protocol – like HTTP, TCP, UDP, IP)
Bullet points 1 and 2
NOW if we are going to develop a protocol, so we’ll need some way to SPECIFY a protocol. How do we do that?
We could write text, but as all know, that’s prone to misinterpretation, and might be incomplete. You might write a specification, and then think “oh yeah – I forgot about that case”
What we need is more formal way to specify a protocol. In fact, with a formal specification there may be ways to PROVE PROPERTIES about a specification. But that’s an advanced topic we won’t get into here. We’ll start here by adopting a fairly simple protocol specification technique known as finite state machines (FSM)
And as the name might suggest, a central notion of finite state machines is the notion of STATE
<talk about state>

## Slide 32: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
rdt_rcv(packet)
Wait for call from below
receiver
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
sender
Wait for call from above
Notes: We’ll start with the simplest case possible - an unreliable channel that is, in fact perfect – no segments are lost, corrupted, dupplicated or reordered. The sender just sends and it pops out the other side(perhaps after some delay) perfectly.

## Slide 33: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum (e.g., Internet checksum) to detect bit errors
the question: how to recover from errors?
How do humans recover from “errors” during conversation?

## Slide 34: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors?
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
stop and wait
sender sends one packet, then waits for receiver response

## Slide 35: rdt2.0: FSM specifications
Wait for call from above
udt_send(sndpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)

## Slide 36: rdt2.0: FSM specification
Wait for call from above
udt_send(sndpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver
Note: “state” of receiver (did the receiver get my message correctly?) isn’t known to sender unless somehow communicated from receiver to sender
that’s why we need a protocol!
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
isNAK(rcvpkt)
isACK(rcvpkt)

## Slide 37: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
udt_send(sndpkt)
udt_send(NAK)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
sender
receiver
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)

## Slide 38: rdt2.0: corrupted packet scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver

## Slide 39: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet, then waits for receiver response

## Slide 40: rdt2.1: sender, handling garbled ACK/NAKs
Wait for call 0 from above
Wait for ACK or NAK 0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt)
&& (corrupt(rcvpkt) ||
isNAK(rcvpkt) )
Wait for
call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
L
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt) && isACK(rcvpkt)
L

## Slide 41: rdt2.1: receiver, handling garbled ACK/NAKs
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 42: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 43: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt
As we will see, TCP uses this approach to be NAK-free

## Slide 44: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 45: rdt3.0: channels with errors and loss
New channel assumption: underlying channel can also lose packets (data, ACKs)
  checksum, sequence #s, ACKs, retransmissions will be of help … but not quite enough
Q: How do humans handle lost sender-to-receiver words in conversation?

## Slide 46: rdt3.0: channels with errors and loss
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
    retransmission will be duplicate, but seq #s already handles this!
    receiver must specify seq # of packet being ACKed
timeout
use countdown timer to interrupt after “reasonable” amount of time

## Slide 47: rdt3.0 sender
Wait for ACK0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
Wait for
call 0 from above
Wait for ACK1
Notes: We see the familiar four state sender from our rdt 2.1 and 2.2 protocols. Top two states when sending packet with zero seq # and bottom two

## Slide 48: rdt3.0 sender
Wait for ACK0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
udt_send(sndpkt)
start_timer
timeout
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
L
rdt_rcv(rcvpkt)
L
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
L
Notes: We see the familiar four state sender from our rdt 2.1 and 2.2 protocols. Top two states when sending packet with zero seq # and bottom two

## Slide 49: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 50: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
ack1
send ack1
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
pkt1
(ignore)
rcv ack1

## Slide 51: Performance of rdt3.0 (stop-and-wait)
example: 1 Gbps link, 15 ms prop. delay, 8000 bit packet
  U sender: utilization – fraction of time sender busy sending
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs
  time to transmit packet into channel:
Notes: if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link
network protocol limits use of physical resources
Let’s develop a formula for utilization

## Slide 52: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 53: rdt3.0: stop-and-wait operation
sender
receiver
Usender
=
L / R
RTT
RTT
L/R
+ L / R
=
0.00027
=
.008
30.008
rdt 3.0 protocol performance stinks!
Protocol limits performance of underlying infrastructure (channel)

## Slide 54: rdt3.0: pipelined protocols operation
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged packets
  range of sequence numbers must be increased
  buffering at sender and/or receiver

## Slide 55: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!
Notes: two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 56: Go-Back-N: sender
sender: “window” of up to N, consecutive transmitted but unACKed pkts
  k-bit seq # in pkt header
cumulative ACK: ACK(n): ACKs all packets up to, including seq # n
  on receiving ACK(n): move window forward to begin at n+1
timer for oldest in-flight packet
timeout(n): retransmit packet n and all higher seq # packets in window
Notes: window size of 14, 8 have been sent but are not yet ackowledgedm 6 sequence numbers are available for us. In woindow, but no calls from above to use them.
Note – we’ll skip the Go-Back-N FSM specification you can chack that out in powerpoitn slides or book)
TCP uses cumulative ACK

## Slide 57: Go-Back-N: receiver
ACK-only: always send ACK for correctly-received packet so far, with highest in-order seq #
  may generate duplicate ACKs
  need only remember rcv_base
on receipt of out-of-order packet:
  can discard (don’t buffer) or buffer: an implementation decision
  re-ACK pkt with highest in-order seq #
rcv_base
received and ACKed
Out-of-order: received but not ACKed
Not received
Receiver view of sequence number space:
…
…
Notes: Note – we’ll skip the Go-Back-N FSM specification (actually it’s

## Slide 58: Go-Back-N in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
pkt 2 timeout
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5
Notes: Let’s skip FSM specification for GBN – check out the book or ppt – and let’s watch GBN sender and receivers in action.
Let assume a window size of 4. at t=0, sender sends packets 0, 1, 2 3, 4, and packet 2 will be lost
At the receiver:
Packet 0 received ACK0 generated
Packet 1 received ACK1 generated
Packet 2 is lost, and so when packet 3 is received, ACK 1 is sent – that’s the cumulative ACK, re-Acknowledging the receipt of packet 1. and in this implementation packet 3 is discarded

## Slide 59: Selective repeat
receiver individually acknowledges all correctly received packets
  buffers packets, as needed, for eventual in-order delivery to upper layer
sender times-out/retransmits individually for unACKed packets
  sender maintains timer for each unACKed pkt
sender window
  N consecutive seq #s
  limits seq #s of sent, unACKed packets
Notes: An important mechanism of GBN was the use of the cumulative acknowledgements, and as we mentioned, cumulative ACKs are used in TCP
An alternate ACK mechanism would be for the receiver to indiviually acknowledge specific packets as they are received. This mechanism is at the heart of the Selective repeat protocol.

## Slide 60: Selective repeat: sender, receiver windows

## Slide 61: Selective repeat: sender and receiver
data from above:
if next available seq # in window, send packet
timeout(n):
resend packet n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark packet n as received
if n smallest unACKed packet, advance window base to next unACKed seq #
sender
packet n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order packets), advance window to next not-yet-received packet
packet n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver
Notes: If the packet is in order, its data will be delivered, as will any buffered data that can now be delived in order

## Slide 62: Selective Repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
send pkt2
(but not 3,4,5)
X
loss
pkt 2 timeout
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
record ack3 arrived
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
Q: what happens when ack2 arrives?

## Slide 63: Selective repeat: a dilemma!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
example:
seq #s: 0, 1, 2, 3 (base 4 counting)
window size=3

## Slide 64: Selective repeat: a dilemma!
Q: what relationship is needed between sequence # size and window size to avoid problem in scenario (b)?
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
example:
seq #s: 0, 1, 2, 3 (base 4 counting)
window size=3
receiver can’t see sender side
receiver behavior identical in both cases!
something’s (very) wrong!

## Slide 65: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 66: TCP: overview RFCs: 793,1122, 2018, 5681, 7323
cumulative ACKs
pipelining:
    TCP congestion and flow control set window size
connection-oriented:
  handshaking (exchange of control messages) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
    one sender, one receiver
reliable, in-order byte steam:
    no “message boundaries"
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
Notes: Typical MSS is 1460 bytes

## Slide 67: TCP segment structure
source port #
dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
sequence number
segment seq #: counting bytes of data into bytestream (not segments!)
application
data
(variable length)
data sent by application into TCP socket
A
acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification

## Slide 68: TCP sequence numbers, ACKs
Sequence numbers:
  byte stream “number” of first byte in segment’s data
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from receiver
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
Acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor

## Slide 69: TCP sequence numbers, ACKs
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: The key thing to note here is that the ACK number (43) on the B-to-A segment is one more than the sequence number (42) on the A-toB segment that triggered that ACK
Similarly, the ACK number (80) on the last A-to-B segment is one more than the sequence number (79) on the B-to-A segment that triggered that ACK

## Slide 70: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT, but RTT varies!
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT:measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 71: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average (EWMA)
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
Notes: This is how TCP re-computes the estimated RTT each time a new SampleRTT is taken.
The process is knows as an exponeitally weighted moving average, shown by the equation here.
<say it>
Where alpha reflects the influence of the most recent measurements on the estimated RTT; a typical value of alpha used in implementaitons is .125
The graph at the bottom show measured RTTs beween a host in the Massachusetts and a host in France, as well as the estimated, “smoothed” RTT

## Slide 72: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT: want a larger safety margin
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
DevRTT = (1-)*DevRTT + *|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
DevRTT: EWMA of SampleRTT deviation from EstimatedRTT:
Notes: Given this value of the estimated RTT, TCP computes the timeout interval to be the estimated RTT plus a “safety margin”
And the intuition is that if we are seeing a large variation in SAMPLERTT – the RTT estimates are fluctuating a lot - then we’ll want a larger savety margin
So TCP computes the Timeout interval to be the Estimated RTT plus 4 times a measure of deviation in the RTT.
The deviation in the RTT is computed as the eWMA of the difference between the most recently measured SampleRTT from the Estimated RTT

## Slide 73: TCP Sender (simplified)
event: data received from application
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK received
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
Notes: Given these details of TCP sequence numbers, acks, and timers, we can now describe the big picture view of how the TCP sender and receiver operate
You can check out FSMs in book; let’s just give an English text description here and let’s start with the sender.

## Slide 74: TCP Receiver: ACK generation [RFC 5681]
Event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
Notes: Rather than immediately ACKnowledig this segment, many TCP implementations will wait for half a second for another in-order segment to arrive, and then generate a single cumulative ACK for both segments – thus decreasing the amount of ACK traffic. The arrival of this second in-order segment and the cumulative ACK generation that covers both segments is the second row in this table.

## Slide 75: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: To cement our understanding of TCP reliability, let’s look a a few retransmission scenarios
In the first case a TCP segments is transmited and the ACK is lost, and the TCP timeout mechanism results in another copy of being transmitted and then re-ACKed a the sender
In the second example two segments are sent and acknowledged, but there is a premature timeout e for the first segment, which is retransmitted. Notet that when this retransmitted segment is received, the receiver has already received the first two segments, and so resends a cumulative ACK for both segments received so far, rather than an ACK for just this fist segment.

## Slide 76: TCP: retransmission scenarios
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: And in this last example, two segments are again transmitted, the first ACK is lost but the second ACK, a cumulative ACK arrives at the sender, which then can transmit a third segment, knowing that the first two have arrived, even though the ACK for the first segment was lost

## Slide 77: TCP fast retransmit
Host B
Host A
timeout
ACK=100
ACK=100
ACK=100
ACK=100
X
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Receipt of three duplicate ACKs indicates 3 segments received after a missing segment – lost segment is likely. So retransmit!
if sender receives 3 additional ACKs for same data (“triple duplicate ACKs”), resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: Let’s wrap up our study of TCP reliability by discussing an optimization to the original TCP known as TCP fast retransmit,
Take a look at this example on the right where 5 segments are transmitted and the second segment is lost. In this case the TCP receiver sends an ACK 100 acknowledging the first received segment.
When the third segment arrives at the receiver, the TCP receiver sends another ACK 100 since the second segment has not arrived. And similarly for the 4th and 5th segments to arrive.
Now what does the sender see? The sender receives the first ACK 100 it has been hoping for, but then three additional duplicate ACK100s arrive. The sender knows that somethings’ wrong – it knows the first segment arrived at the receiver but three later arriving segments at the receiver – the ones that generated the three duplicate ACKs – we received correctly but were not in order. That is, that there was a missing segment at the receiver when each of the three duplicate ACK were generated.
With fast retransmit, the arrival of three duplicate ACK causes the sender to retransmit its oldest unACKed segment, without waiting for a timeout event. This allows TCP to recover more quickly from what is very likely a loss event
specifically that the second segment has been lost, since three higher -numbered segments were received

## Slide 78: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 79: TCP connection management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters (e.g., starting seq #s)
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
Notes: The other TCP topic we’ll want to consider here is that of “connection management”
The TCP sender and reciver have a number of pieces of shared state that they must establish before actually communication
FIRST theym ust both agree that they WANT to communicate with each other
Secondly there are connection parameters – the initial sequence number and the initial receiver-advertised bufferspace that they’ll want to agree on
This is done via a so-called handshake protocol – the client reaching our to the server, and the server answering back.
And before diving into the TCP handshake protocol, let’s first consider the problem of handshaking, of establishing shared state.

## Slide 80: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
Notes: Here’s an example of a two way handshake. Alice reaches out to Bob and say’s “let’s talk” and Bob says OK, and they start their conversation
For a network protocol, the equivalent protocol would be a client sending a “request connection” message saying ”let’s talk, the initial sequence number is x”
And the server would respond with a message ”I accept your connect x”
And the question we want to ask ourselves is <talk through>
Will this work? Let’s look at a few scenarios…

## Slide 81: 2-way handshake scenarios
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
ACK(x+1)
No problem!

## Slide 82: 2-way handshake scenarios
ESTAB
retransmit
req_conn(x)
req_conn(x)
client terminates
server
forgets x
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
acc_conn(x)
Problem: half open connection! (no client)

## Slide 83: 2-way handshake scenarios
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
Problem: dup data
accepted!
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
retransmit
req_conn(x)
ESTAB
req_conn(x)

## Slide 84: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
Client state
LISTEN
Server state
LISTEN
clientSocket = socket(AF_INET, SOCK_STREAM)
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind((‘’,serverPort))
serverSocket.listen(1)
connectionSocket, addr = serverSocket.accept()
clientSocket.connect((serverName,serverPort))
Notes: TCP’s three way handshake, that operates as follows
Let’s say the client and server both create a TCP socket as we learned about in Chapter 2 and enter the LISTEN state
The client then connects to the server sending a SYN message with a sequence number x (SYN Message is an TCP Segment with SYN but set in the header – you might want to go back and review the TCP segment format!)
The server is waiting for a connection, and receives the SYN message enters the SYN received state (NOT the established state and sends a SYN ACK message back.
Finally the client sends an ACK message to the server, and when the server receiver this enters the ESTABLished state. This is when the application process would see the return from the wait on the socket accept() call

## Slide 85: Closing a TCP connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled
Notes: All good things must come to an end, and that’s true for a TCP connection as well.
And of course there’s a protocol for one side to gracefully close of a TCP connection using a FIN message, to which the other side sends a FINACK message and waits around a bit to respond to any retransmitted FIN messages before timing out.

## Slide 86: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 87: Principles of congestion control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
manifestations:
  long delays (queueing in router buffers)
  packet loss (buffer overflow at routers)
different from flow control!
congestion control: too many senders, sending too fast
flow control: one sender too fast for one receiver
a top-10 problem!

## Slide 88: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from observed loss, delay
data
data
ACKs
ACKs
approach taken by TCP

## Slide 89: Approaches towards congestion control
TCP ECN, ATM, DECbit protocols
data
data
ACKs
ACKs
explicit congestion info
Network-assisted congestion control:
routers provide direct feedback to sending/receiving hosts with flows passing through congested router
may indicate congestion level or explicitly set sending rate

## Slide 90: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 91: TCP congestion control: AIMD
approach: senders can increase sending rate until packet loss (congestion) occurs, then decrease sending rate on loss event
AIMD sawtooth
behavior: probing
for bandwidth
TCP sender Sending rate
time
  increase sending rate by 1 maximum segment size every RTT until loss detected
Additive Increase
  cut sending rate in half at each loss event
Multiplicative Decrease

## Slide 92: TCP AIMD: more
Multiplicative decrease detail: sending rate is
Cut in half on loss detected by triple duplicate ACK (TCP Reno)
Cut to 1 MSS (maximum segment size) when loss detected by timeout (TCP Tahoe)
Why AIMD?
AIMD – a distributed, asynchronous algorithm – has been shown to:
  optimize congested flow rates network wide!
  have desirable stability properties

## Slide 93: TCP congestion control: details
TCP sender limits transmission:
cwnd is dynamically adjusted in response to observed network congestion (implementing TCP congestion control)
LastByteSent- LastByteAcked
<
cwnd
last byte
ACKed
last byte sent
cwnd
sender sequence number space
available but not used
TCP sending behavior:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
TCP rate
~
~
cwnd
RTT
bytes/sec
sent, but not-yet ACKed
(“in-flight”)

## Slide 94: TCP slow start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
Host A
one segment
Host B
RTT
time
two segments
four segments
summary: initial rate is slow, but ramps up exponentially fast

## Slide 95: TCP: from slow start to congestion avoidance
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
X